## Slide 1: MEF Reference Presentation November 2011
MEF 20: User Network Interface Type 2
With Testing Support via MEF 21, etc.

## Slide 2: Topics
The presentation covers
  Carrier Ethernet expansion and the need for MEF 20
  MEF 20 Overview
    Impact of MEF 20 on the market and Carrier Ethernet
  Technical Review
    Functionality and Scope of MEF 20
    The MEF UNI
    Implementation options
    Relationship to other specifications and standards
  Comparison with legacy solutions
  Timing of MEF 20 and other related MEF work
  Testing MEF 20 (using MEF 21)
  Summary

## Slide 3: MEF 20 Advances Carrier Ethernet Deployment
MEF 20
Introduces automated processes for managing services, fault monitoring and management enabling
  Carrier Ethernet networks to scale
  Carrier Ethernet networks to operate at reduce cost and
  Creation of a framework for the dynamic service provisioning that will leverage the inherent benefits of MEF-defined Carrier Ethernet services

## Slide 4: MEF 20 Overview
MEF 11 introduced 3 types of UNI
  UNI Type 1 (now defined in MEF 13)
    Service Provider and Customer manually configure the UNI-N and UNI-C for services.
  UNI Type 2 (now defined in MEF 20)
    An automated implementation model allowing UNI-C to retrieve EVC status and configuration information from UNI-N
    Enhanced UNI attributes
    Additional fault management and protection functionality
    Backward compatibility with UNI Type 1
  UNI Type 3 (Possible future MEF Specification)
    Allows the UNI-C to request, signal and negotiate EVCs and its associated Service Attributes to the UNI-N. UNI
    Type 3 is for further study.

## Slide 5: How MEF 20 UNI Type 2 Impacts the Market
Enterprise and Business
  Users will have faster response to their changing requirements driven by the breadth and automation of service management
  Users will benefit from increased service level performance visibility
Service Providers
  Will benefit from faster time to revenue
  Reduction in high cost error-prone processes
  Improved customer satisfaction and retention
Equipment Manufacturers
  Implementing MEF 20 will bring new revenue opportunities
NEMs
SPs, MSOs
Enterprise
SMB
Residential

## Slide 6: Technical Review

## Slide 7: Functionality and Scope of MEF 20
Ethernet Local Management Interface (E-LMI)
  Allows UNI-C to retrieve EVC status and service attributes from UNI-N as specified in MEF 16
Link OAM (Operation, Administration and Management)
  Allows customer and service provider to monitor and diagnose the UNI connectivity via Link OAM (link level)
Service OAM
  Allows customer and service provider to monitor and diagnose the UNI connectivity via Service OAM (end-to-end)
Protection
  Capability to protect UNI against port failure via Link Aggregation protocol
Enhanced UNI Attributes
  Such as bandwidth profile per egress UNI, Maximum Transfer Unit size, etc. as defined in MEF 10., MEF 6.1
L2CP Handling
  Governs the passing or filtering of Layer 2 control protocols to the Ethernet Virtual Connections
Details of each mandatory and optional element are to be found in the specification

## Slide 8: The MEF User Network Interface
Service provider responsibility
UNI
Carrier Ethernet Network
The User Network Interface (UNI)
  The UNI is the single point that is the demarcation between the customer and the service provider/Cable Operator/Carrier/MSO
  The UNI is typically at a port on an active device owned and operated by the Service Provider
  The UNI in a Carrier Ethernet Network uses a physical Ethernet Interface at operating speeds 10Mbs, 100Mbps, 1Gbps or 10Gbps
CE: Customer Equipment, UNI: User Network Interface. MEF certified Carrier Ethernet products
CE
  In this instance the UNI is located at the port of the service provider edge device located in the customer premises.
  The service provider “cloud” is shown terminating in the customer premises
customer responsibility

## Slide 9: Functional Elements of the UNI
Service provider responsibility
UNI
There are two functional elements (typically*) located in two connected devices situated on either side of the UNI demarcation point:
    UNI-C: Executes the processes of the customer side
    UNI-N: Executes the processes of the network side
    * All the functions of the UNI-N and UNI-C need not be located in the same physical device as they may be located in several devices
CE: Customer Equipment, UNI: User Network Interface. MEF certified Carrier Ethernet products
CE
customer responsibility
UNI-C
UNI-N
Carrier Ethernet Network

## Slide 10: MEF 20 in the context of MEF 13
MEF 13: UNI Type 1 Implementation Agreement
  Approved in November 2005
  UNI Type 1.1 and 1.2 are defined
  Type 1.1 : Non-multiplexed UNI for Services like EPL
  Type 1.2 : Multiplexed UNI for Services like EVPL
  S.P. and customer manually configure the UNI-N and UNI-C for services
MEF 20 extends this …

## Slide 11: MEF 20 Implementation Options
MEF 20 Specifies phased/alternate implementation. This allows quicker time to market and faster time to revenue for all concerned
UNI Type 2.1
Mandatory Features
  Backward comp. to UNI Type 1
  Service OAM
  Enhanced UNI attributes
  L2CP handling
Optional Features
  Link OAM
  Protection
  E-LMI
UNI Type 2.2
Mandatory Features
  Backward comp. to UNI Type 1
  Service OAM
  Enhanced UNI attributes
  L2CP handling
  Link OAM
  Protection
  E-LMI

## Slide 12: Relationship to Other MEF and Industry Standards
Why has the MEF undertaken the initiative?
  This exactly in line with the MEF’s mission to undertake work that helps accelerate the adoption of Carrier Ethernet and to use other existing standards wherever practical
  The MEF maintains standing liaisons with these industry standards bodies
Function | Source
MEF 20 Implementation Agreement is an enhancement to UNI Type 1 | MEF13
Functionality includes capability for UNI-C to retrieve EVC status & configuration of service attributes from UNI-N via E-LMI | MEF16
Capability for customer and service provider to examine UNI connectivity via Link OAM | Clause 57 of IEEE 802.3
Capability for customer and service provider to examine UNI connectivity via Service OAM | ITU-T Y.1731 and IEEE 802.1ag
Capability to protect UNI against port failure via Link Aggregation | Clause 43 of IEEE 802.3

## Slide 13: How Does MEF 20 Compare with Legacy Solutions?
Comparison
  The addition of UNI type 2 functionality is comparable to baseline functionality of other legacy technologies
However …
  MEF 20 now enables the flexibility, service granularity and cost benefits of Carrier Ethernet not present in less flexible or lower bandwidth legacy solutions

## Slide 14: Timing of MEF 20 & Relationship to MEF Work
MEF Specifications nearing completion
  E-NNI
  Network Interface Devices
Other MEF Initiatives
  Wholesale Access Interconnect
  Service Assurance
  Access Group Initiatives
Timing of MEF 20 is very relevant
  Operational Scalability is moving on to the critical path for Carrier Ethernet growth
MEF 20 is one of several initiatives related to operational effectiveness of, scalability and expansion of Carrier Ethernet

## Slide 15: Testing UNI Types 1 & 2
MEF 20
UNI Type 2
Implementation Agreement
MEF 27 - Abstract Test Suite For UNI Type 2 Part 5: Enhanced UNI Attributes & Part 6: L2CP Handling
Abstract Test Suite for UNI Type 2 Part 4: Protection
MEF 25 - Abstract Test Suite for UNI Type 2 Part 3 Service OAM
MEF 24 - Abstract Test Suite for UNI Type 2 Part 2 E-LMI
MEF 21
Abstract Test Suite for UNI Type 2 Part 1: Link OAM
MEF 13
UNI Type 1
Implementation Agreement
MEF 19
Abstract Test Suite for UNI Type 1
MEF 11
User Network Interface (UNI) Requirements and Framework
First Testing of MEF 20 is specified in MEF 21
Thorough testing is reflected in large number of test cases
Further Test projects are in preparation
E-NNI will leverage MEF 21 test cases
MEF Certification will be decided in due course

## Slide 16: MEF Development Work
Future Technical Work
  The MEF technical work continues on all elements of Carrier Ethernet (OAM, Network to Network Interfaces, implementation agreements, etc.) This includes coordination with other standards bodies.
Deployment now brings immediate benefits
  Immediate benefits are being obtained today based on implementing today’s specifications. These benefits increase as the specifications complete
MEF Timescales
  The MEF continues to exist during the foreseeable future to complete its mission

## Slide 17: MEF 20 Summary
MEF 20’s scope and new management functions will
  Accelerate deployment
  Reduce OpEx and accelerate revenue for service providers
  Bring increased customer satisfaction
  Provide new opportunities for equipment manufacturers
MEF 20 is a timely addition given the rapid growth of Carrier Ethernet in the market

## Slide 18: MEF Reference Presentations
MEF Reference Presentations Covering the Principal Work of the MEF | 
Overview presentation of the MEF. | This presentation gives basic and most up-to-date information about the work of the MEF. It also introduces the definitions, scope and impact of Carrier Ethernet, the MEF Certification programs and describes the benefits of joining the MEF.
Overview presentation of the Technical Work of the MEF | Includes a summary of the specifications of the MEF, structure of the technical committee, work in progress and relationships with other Industry Standards bodies. For PowerPoint overviews of individual specifications: click here
Carrier Ethernet Services Overview | This presentation defines the MEF Ethernet Services that represent the principal attribute of a Carrier Ethernet Network
Carrier Ethernet User-Network Interface | This presentation discusses the market impact of MEF 20: UNI Type 2 Implementation agreement
Carrier Ethernet Access Technology Overview | This presentation describes how the MEF specifications bring Carrier Ethernet services to the world's Access networks (with examples of Active Ethernet (Direct Fiber), WDM Fiber, MSO Networks(COAX and Direct Fiber), Bonded Copper, PON Fiber and TDM (Bonded T1/E1, DS3/E3))
Carrier Ethernet Interconnect Program. | This is the latest presentation from the Carrier Ethernet Interconnect Working Group which acts as a framework for all presentations given on this topic.
Carrier Ethernet OAM & Management Overview | This presentation describes the management framework and the OAM elements for fault and performance management expressed in terms of the life cycle of a Carrier Ethernet circuit
Carrier Ethernet for Mobile Backhaul | A comprehensive marketing and technical overview of the MEF's initiative on Mobile Backhaul that has lead to the adoption of Carrier Ethernet as the technology of choice for 3G and 4G backhaul networks
Carrier Ethernet Business Services | A comprehensive presentation aimed at business users
The MEF Certification Programs | A presentation of the MEFs three certification programs: Equipment, Services and Professionals. These programs have been a cornerstone of the success of Carrier Ethernet and its deployment in more than 100 countries around the world.
Presentations may be found at http://metroethernetforum.org/Presentations

## Slide 19: End of Presentation