## Slide 1: Optimizing Mobile Backhaul
MEF Reference Presentation
October 2011

## Slide 2: Two Implementations of Carrier Ethernet
Application of Carrier Ethernet for End-to-End Carrier Ethernet Network Service Delivery
Service Provider 1
Aka Retail Provider
CE
UNI
End User Subscriber Site
UNI
CE
ENNI
Service Provider 2
Aka Access Provider
End User Subscriber Site
EVC
E-Access
Service Provider
aka Mobile Operator
RAN NC Site
UNI
Service Provider
aka Access or Backhaul Provider
EVC
RAN CE
Application of Carrier Ethernet for Mobile Backhaul Network
UNI
RAN CE
RAN Base Station Site
Customer (Subscriber) is Mobile Operator
Context for this Presentation
* Full details in MEF Mobile Backhaul Reference Presentation

## Slide 3: MEF Reference Presentations
Intention
  These MEF reference presentations are intended to give general overviews of the MEF work and have been approved by the MEF Marketing Committee
  Further details on the topic are to be found in related specifications, technical overviews, white papers in the MEF public site Information Center: http://metroethernetforum.org/InformationCenter
  Notice
  © The Metro Ethernet Forum 2011. Any reproduction of this document, or any portion thereof, shall contain the following statement: "Reproduced with permission of the Metro Ethernet Forum." No user of this document is authorized to modify any of the information contained herein. See also MEF Terms of use at http://metroethernetforum.org/page_loader.php?p_id=501

## Slide 4: Mobile Backhaul Topics
Market Impact of Carrier Ethernet for Mobil Backhaul
  Market Data and Drivers
  MEF 22 – Mobile Backhaul Implementation Agreement Phase I
New Work
  Carrier Ethernet for MBH: 2011-2014
  Work in progress supporting 4G (MBH IA Phase II)
  Carrier Ethernet Multiple Classes of Service in the Mobile Backhaul
    Optimizing the Backhaul
  Synchronization for Mobile Backhaul
    A New MEF Paper
Addendum: Migration from Legacy Transport
Carrier Ethernet for Mobile Backhaul
Engineering Cost-efficient Mobile Backhaul

## Slide 5: Mobile Backhaul Market Scorecard
IP/Ethernet mobile backhaul (MBH) is the universally accepted solution to lower the costs of growing mobile data traffic, include IP/Ethernet in the 3G transition, and use IP as the basic technology of LTE and WiMAX
The momentum is growing no matter how it is measured:
150 mobile operators are now actively deploying IP/Ethernet backhaul
89% of 2010 mobile backhaul equipment spending was for IP/Ethernet
  79% of operators have a strategy to move to single all-IP/Ethernet backhaul
  Timing/synchronization is no longer a barrier
Source: Infonetics Research, Mobile Backhaul Equipment and Services Biannual Market Size, Share, and Forecast, April 2011

## Slide 6: MBH 2008-2010: Why MBH Went Ethernet
The 2008 - 2010 story
Mobile bandwidth is growing exponentially – but revenues are not.
Carrier Ethernet for Mobile Backhaul
Ethernet offers significantly lower cost/bit
Ethernet is ubiquitous, simple and flexible
Ethernet opens up wholesale opportunities
“Ethernet is seen as the only solution for next generation MBH networks … legacy technology can’t scale … “
Michael Howard, principal analyst at Infonetics Research

## Slide 7: MEF 22 – Mobile Backhaul Implementation Agreement
Approved Specification
Approved Draft
Letter Ballot
Working Document
Straw Ballots
New Project

## Slide 8: MEF 22: Overview
TDM to IP/Eth
Industry trends
Other SDOs
MEFs own work as the foundation
Standardized
reference
points
Service
Requirements
(Service Types,
CoS, Eth OAM, etc)
Synchronization
Recommendations
MEF 10.x
MEF 6.x
MEF 13
MEF 20
Notes: The IA relies on MEF specifications – services, attributes, interface, management, etc.
Also, consistent with other SDO’s work – example, ITU-T or NGMN’s work.
The IA applies the body of work to the use case of Mobile Backhaul for interoperable implementations between:
Vendor equipment
MEN Operator and Mobile Operator operations

## Slide 9: MEF 22 Terminology and Concepts
Functional Elements as defined in MEF 22 Specification
Carrier Ethernet Mobile Backhaul Service
Standard Demarcation
Standard & Scalable Services with Quality of Service
Service Management & Reliability
RAN | Radio Access Network
RAN BS | RAN Base Station
RAN NC | RAN Network Controller
RAN CE | RAN Customer Edge –Mobile network node/site
RNC | Radio Network Controller
Service Provider
UNI
RAN CE
UNI
RAN BS
UNI
RAN BS
RAN NC
RAN CE
RAN CE
RAN NC
RAN CE
UNI
Customer (Subscriber) is Mobile Operator & needs Mobile Backhaul between RAN CEs
Service Provider (SP) offers Mobile Backhaul Service between demarcation points
Standard Demarcation
Notes: The RAN CE is a generic term that identifies a mobile network node or site, such as a RAN network Controller or RAN Base Station
A RAN NC may be a single network controller or a site composed of several network elements including: OSS, WCDMA Radio Network Controller or Synchronization Server.
Customer (Subscriber) = Mobile Operator, ie., one who purchases the backhaul service between CES
Service Provider or Operator = one who offers the Mobile Backhaul service between demarcation between customer and SP
Important to note: demarcation of responsibility between customer and SP
Important to note: scope of responsibility for Mobile Operator is RAN CE to RAN CE
Important to note: scope of responsibility for SP is demarcation to demarcation, ie., UNI to UNI.
What services? ….and what are the key attributes of the service?

## Slide 10: MEF Services over multiple Access Technologies
Backhaul Service Provider
Direct Fiber
Ethernet Demarcation: MEF User to Network Interface (UNI)
TDM Demarcation: Generic Interworking Function (GIWF)
Microwave
Ethernet over Bonded PDH (E1/DS1)
Bonded Copper
BTS/NodeB
BTS/NodeB
BTS/NodeB
BTS/NodeB
N x GigE
Wireless CO
(RNC)
ONT
BTS/NodeB
Splitter
PON Fiber
Notes: 10
10
Transition to explaining how
MEF 6 and MEF 8 services need to be supported
same SP but with different access technologies in different parts of the SP’s network cloud.
same cell site location might have to migrate from existing 2G with TDM demarcation
- A SP will need to support both TDM and Ethernet demarcation
Note: A SP’s scope is demarcation to demarcation
SP can use multiple access technologies within SP’s cloud to support all MEF services.

## Slide 11: New MEF Work

## Slide 12: MBH 2011-2014: Optimizing the Backhaul
Ethernet has been adopted: there are new challenges
4G/LTE
  MEF providing necessary attributes required: MEF 22.1
  Enhanced Service Attributes
Single Class of Service causes very costly overbuild
  Initial and Current deployment dominated by inefficient single class of service implementation
  MEF providing specifications and guidance for deploying multiple classes of service
Help with best Practices for Synchronization
  New MEF paper available October 2011
Total Impact of new MEF work
  Efficient, profitable and scalable deployment for Mobile Operators Access Providers

## Slide 13: Mobile Backhaul Service for LTE
3G Backhaul: ~ 100km (Metro)
LTE Backhaul:
  BS to S-GW/MME ~1000km (Regional)
  BS to BS ~ neighbors (10s of km)
RNC
Metro
Regional
S-GW
MME
CEN
CEN
EVC for X2 Interface
EVC for S1 Interface
S-GW
MME
S1-flex
S-GW
MME

## Slide 14: Enhanced Service Attributes for Mobile Backhaul
Carrier Ethernet Network
UNI
RAN BS
RAN NC
UNI
RAN BS
UNI
PRC

## Slide 15: Enhancements: Service Class for sync traffic
Using Service Frames in the EVC
  Frame arrival rate with Adaptive Clock Recovery (ACR)
    Stringent performance, egg. Frame Delay Range
  Can also use CES RTP optional header for synchronization timestamps
Using a control protocol (e.g. IEEE1588v2)
  Separate Class of Service with stringent performance, if needed
UNI
EVC
CoS (Data)
CoS (Sync)
UNI
EVC_(Sync)
EVC (Data)
Sync as a Class of Service (EVC)
Sync as a Class of Service (EVC+PCP)
UNI
EVC
Frame Arrival
MO: Mobile Operator
NE: Network Element
PEC: Packet Equipment Clock
PRC: Primary Reference Clock
PCP: Priority Code Point
Notes: Mobile Operator can use packet method to distribute clock information from controller site to base station sites
May want a service across MEN with stringent performance, e.g.., minimum Frame Delay Range
MEN Operator can provide a CoS instance (identified as EVC or EVC+PCP) with higher forwarding priority to minimize FDR
Enhancements: recommend a separate CoS and also objectives for this CoS (work in progress)

## Slide 16: Enhancements: UNI Mode Attribute
UNI PHY
  Synchronous mode of operation (Synchronous Ethernet)
    Locked to Ethernet Equipment Clock (EEC)
Interoperable operation of Synchronous Ethernet
  Synchronous messages: Generation & processing rules
  Clock Quality Level (QL) indication & processing rules
  Direction of clock distribution: MEN to Base Station
Recommendation to support QL processing in Base Station
  Failure conditions & Switchover to alternate Primary reference
Notes: UNI PHY needs to be capable of Synchronous mode of Operation – Synchronous Ethernet
locked to EEC for low p-p jitter
Also, interoperability is very important. Why? The two ends of the UNI is in different domains – MEN Operator vs Mobile Operator.
  Details on message processing as well as when and how QL is used
Of course, interface limits are specified when it is a chain of EECs or when a mix of PECs and EECs are used across the MEN.

## Slide 17: Enhancements: Resiliency Performance
Resiliency Performance depends on both UNI and EVC
UNI Resiliency with Link Aggregation (UNI Type 2)
Diversity for higher Availability
  MEN Resiliency Model vs RAN Resiliency Model
  Partial vs Full Diversity
  Use Case: S1-flex in LTE
  Use Case: Multiple Primary Reference Clocks
Group Availability: e.g. Set of EVCs
Notes: Resiliency performance is critical for higher availability
One of the significant additions to the spec is diversity requirements
Eg. two EVCs must be fully diverse including UNIs on different NEs.
The diversity requirement is relevant in LTE
  S1-flex: each BS is connected to two S-GW/MME sites
  Packet method for sync: Each BS’s slave clock is connected to 2 or more Primary Reference Clocks
We already have, in MEF 10.2.1, the Availability for an EVC
In MEF 22.1 we have ‘group availability’, ie., at least 1 EVC is alive.

## Slide 18: Resiliency/Protection
MEF Service Specifications augment industry standards
In totality, they address port and service protection, fault detection and restoration
  At the UNI ports
  At the ENNI (for direct and Exchange connections)
  For UNI to UNI (EVCs)
  UNI-ENNI OVCs
The following is one option for Mobile Backhaul showing Active/Standby
Protection
1+1 APS
LAG (802.1ax LACP)
Dual Homing
Ring (G.8032)
Linear Protection (G.8031)

## Slide 19: Enhancements: Class of Service Mapping
CoS Name | Example of Generic Traffic Classes mapping into CoS |  | 
 | 4 CoS Model | 3 CoS Model | 2 CoS Model
Very High (H+) | Synchronization | - | -
High (H) | Conversational, Signaling and Control | Conversational and Synchronization, Signaling and Control | Conversational and Synchronization, Signaling and Control, Streaming
Medium (M) | Streaming | Streaming | -
Low (L) | Interactive and Background | Interactive and Background | Interactive and Background
Value to Mobile Operator: Know what performance each 3GPP traffic class will get
Value to MEN Operator: Standard CoS offering with default performance objectives
Notes: In addition to the ‘separate’ CoS, H+, for sync traffic class
MEF 23.x has specified 3 CoS Names: H/M/L – identified by specific PCP/DSCP values at the UNI.
Recommendation for Mobile Operator to map 3GPP service classes to these H/M/L CoS instances
Helps MO understand what performance each traffic class will get
Helps MEN operator to design network to support these standard CoS with default performance objectives.

## Slide 20: Enhancements: Performance objectives
Performance Attributes | CoS Label H |  | CoS Label M |  | CoS Label L1 |  | Applicability
 | Pt-Pt | Multipoint | Pt-Pt | Multipoint | Pt-Pt | Multipoint | 
FD (ms) | £ 10 | TBD | £ 20 | TBD | £ 37 | TBD | At least one of either FD or MFD required
MFD (ms) | £ 7 | TBD | £ 13 | TBD | £ 28 | TBD | 
IFDV (ms) | £ 3 | TBD | £ 8 or N/S 2 | TBD | N/S | TBD | At least one of either FDR or IFDV required
FDR (ms) | £ 5 | TBD | £ 10 or N/S 2 | TBD | N/S | TBD | 
FLR (ratio) | £ .01% i.e. 10-4 | TBD | £ .01% i.e. 10-4 | TBD | £ .1% i.e. 10-3 | TBD | 
Availability | TBD | TBD | TBD | TBD | TBD | TBD | 
[Reference: CoS IA Ph2] Performance Tier 1 (Metro) CoS Performance Objectives
one-way
Note:
- Performance Tier 2 (regional) is also applicable for Mobile Backhaul
- Performance Objective for H+ Class is work in progress
Notes: Explain that these objectives are
For pt-pt only at this time
These are 1-way
Across a performance tier 1, ie., metro scope ~250km max
From a MBH perspective
PT 2 (regional) is also applicable.
H+ CoS objectives is TBD.
Who is responsible to meet these objectives? MEN Operator, of course.
For what? EVC
Scope of these objectives? EVC MEG

## Slide 21: Enhancements: Service Management
Subscriber MEG for Mobile Operator (as Customer/Subscriber)
EVC MEG (or Operator MEG) for MEN Operator (as Service Provider)
  Fault and Performance Management to report EVC Performance
UNI MEG used to monitor MEF compliant UNI
  e.g.. RAN CE & MEN using UNI Type 2 with Service OAM capability
EVC MEG
Notes: A MEN Operator uses the EVC MEG (UNI to UNI) to perform Fault and Performance management.
MEF defines various MEGs in the SOAM FM IA.
This IA has specified who uses what MEGs  implication is need to have capability to support the MEGs.
MO can also do performance measurements from their RAN CEs using Service OAM using Y.1731 protocols. They can use the information to adjust traffic flow between EVCs, for example.

## Slide 22: Enhancements: Resiliency Performance
Resiliency Performance depends on both UNI and EVC
UNI Resiliency with Link Aggregation (UNI Type 2)
Diversity for higher Availability
  MEN Resiliency Model vs RAN Resiliency Model
  Partial vs Full Diversity
  Use Case: S1-flex in LTE
  Use Case: Multiple Primary Reference Clocks
Group Availability: e.g.. Set of EVCs
Notes: Resiliency performance is critical for higher availability
One of the significant additions to the spec is diversity requirements
Eg. two EVCs must be fully diverse including UNIs on different NEs.
The diversity requirement is relevant in LTE
  S1-flex: each BS is connected to two S-GW/MME sites
  Packet method for sync: Each BS’s slave clock is connected to 2 or more Primary Reference Clocks
We already have, in MEF 10.2.1, the Availability for an EVC
In MEF 22.1 we have ‘group availability’, ie., at least 1 EVC is alive.

## Slide 23: Enhancements: Resiliency Performance
Long term disruptions
  EVC Performance attribute: Availability
  Example: performance over a month
Short term disruptions (1 or more Dt intervals)
  EVC Performance attribute: High Loss Interval (HLI) count
    similar to Severely Errored Seconds (SES) in SONET/SDH
  Why: 1-2s loss in signaling can bring down a cell site
When A=1
Count HLIs
Reference: MEF 10.2.1
Notes: Mobile Operators would like a means to characterize the short term disruptions
Understand how many times in a month there were ‘events’ that resulted in high loss state and also the duration of each of those events (consecutive high loss)
Similar to SES in sonet/sdh.
The count is made during those time intervals when A=1, ie., available state for the EVC.
A mobile backhaul service with lots of such disruptions (high loss state) is bad since a 1-2s disruption can bring down the cell site – signaling loss.

## Slide 24: MEF 22 Scope Comparison
ITEM | PHASE 1 | PHASE 2
UNI |  | 
Service Types |  | 
Link OAM |  | 
Service OAM FM |  | 
Service OAM PM |  | 
CoS |  | 
Performance recommendations |  | 
Packet based sync |  | 
SyncE |  | 
Resiliency Performance |  | 
GSM, WCDMA, CDMA2000, WiMAX 802.16e |  | 
LTE |  | 
Notes: This slide is to
put in to context the breadth of coverage
Also, additional depth in previously covered topics
Question: Do MEN Operators and Mobile Operators see any gaps? What and Why?

## Slide 25: A few key Service Attributes
UNI Type (MEF 13 & 20)
UNI Service Attributes (MEF 10.2, MEF 6.1)
  Mode: Asynchronous Full Duplex
  >1 EVC & capability to support max # of EVCs
  Bandwidth profiles per UNI
EVC per UNI Service Attributes (MEF 10.2, MEF 6.1)
  EVC Classification: CE-VLAN ID to EVC Map
  Bandwidth profiles per EVC
EVC Service Attributes (MEF 10.2, MEF 6.1, MEF 23)
  EVC Type and UNI List with Type (Root or Leaf)
  CE-VLAN and Class of Service (CoS) preservation
  EVC Performance per CoS ID for one or more Classes of Service
Notes: Use this to explain the key attribute and also to highlight what enhancements
When discussing a MEF 6 (EVC based) service for Mobile Backhaul
Important to understand what the key attributes of the service are
A MEF service is a combination of the EVC and the UNIs associated by that EVC.
MEF compliant UNIs should be available on equipment owned by Mobile Operator and Service Provider/MEN.
Depending on the service(s) required one can then configure key service attributes for UNI and EVC
Examples:
how many EVCs at a given UNI
How many classes of service
how customer traffic is identified and mapped as a specific service
Is there some information that needs to be preserved
How much of the traffic is accepted
What performance is agreed to in the Service Level Specification (SLS)
Etc..
Mobile Backhaul Services can have stringent performance requirements

## Slide 26: Optimizing Mobile Backhaul
Carrier Ethernet with Multiple Classes of Service

## Slide 27: Delivering Bandwidth Required for 4G/LTE
According to all wireless operators, delivering the bandwidth required in the 4G-LTE wireless backhaul is “the single biggest challenge and operating cost in the industry.”
Carrier Ethernet with Multiple Classes of Service represents a breakthrough in sustainable, high-quality, profitable deployment
New Work from the MEF provides
  Two MEF technical specifications in Jan 2012 time frame
    Mobile Backhaul Phase 2
    Class of Services Phase 2
  Business and technical education and Implementation guidance

## Slide 28: Single Class vs. Multi Classes (1)
Result/Impact
Extremely costly – needs massive overbuild
Does not scale - recipe for going out of business
High Priority traffic subject to delay – especially during traffic bursts and peaks
An Access Provider EVC
All one Class of Service: simple but costly
Access Provider
Bursty, delay & loss tolerant data
Delay-sensitive real time data
Mobile Operator
Notes: Prioritizing Data: 1. Network control 2. Interactive voice, video, 3. Signaling, 4 Internet data, business data, streamed video

## Slide 29: Single Class vs. Multiple Classes of Service (2)
Backhaul Operators (aka Access Providers)
More Revenue for same cost: more users supported, more responsive QoS
Avoids costly over-building network to ensure integrity, QoS
Squeezes best performance to maximize profitability by leveraging the statistical multiplexing of Ethernet
Mobile Operators:
  Enables resolution of their most critical challenge:
  “Handling unprecedented growth of data efficiently while preserving or improving QoS.”
Result/Impact
An Access Provider EVC
Mobile Operator
Prioritizing Data: 1. Network control 2. Interactive voice, video, 3. Signaling, 4 Internet data, business data, streamed video
High Priority Lane
Low Priority Lane
Bursty, delay & loss tolerant data
Delay-sensitive real time data
Multiple-Classes of Service: more complex but great rewards

## Slide 30: Frequency Synchronization for Mobile Backhaul
Carrier Ethernet Network
UNI
RAN BS
RAN NC
UNI
RAN BS
UNI
PRC

## Slide 31: Synchronization Requirements
Mobile Network Architecture | Frequency Sync | Time-of-day / Phase Sync
CDMA2000 |  | 
GSM |  | 
UMTS-FDD |  | 
LTE-FDD |  | 
UMTS-TDD |  | 
LTE-FDD with MBMS-Single Freq. Network |  | 
LTE-TDD |  | 
Mobile WiMAX |  | 
TD-SCDMA |  | 
TA=1/fA
TB=1/fB
fA=fB
Frequency Synchronization
A
B
t
t
TA=1/fA
TB=1/fB
fA=fB
Phase Synchronization
A
B
01:00:00
TA=1/fA
TB=1/fB
fA=fB
Time Synchronization
01:00:10
01:00:00
01:00:10
A
B
t
t
t
t
Notes: Explain Mobile Technologies and synchronization requirements
Some require only Frequency and some require phase/time-of-day.
Briefly mention the typical requirements for
- frequency, eg., well known 50ppb for the ‘radio interface’.
Phase can be 2-3 microseconds of difference between BS.
Some Mobile Operators may have GPS at all base stations. Even then they might prefer backup methods.
Conclusion: Mobile Backhaul Service by MEN Operator has to be offered along with
options to distribute frequency and phase synchronization
traceable to a primary reference clock.

## Slide 32: Synchronization Distribution Methods
Distributed (GPS)
Centralized (PRC) and chain of Equipment Clocks (ECs)
  Physical Layer (legacy): SONET/SDH Equipment Clock (SEC)
  Physical Layer: Ethernet Equipment Clock (EECs)
  Packet Equipment Clocks (PECs) with timestamps (1588v2) or frame arrival rate (Adaptive Clock Recovery (ACR))
For RAN CEs with MEF UNIs (Ethernet)
Legacy RAN CE
In Scope
Performance:
Interface Limits for Jitter & Wander at demarcation
Enhancement of UNI attributes?
Notes: Explain the methods:
GPS and SEC is not the focus of this IA
EECs and PECs are in scope.
Note: distribution architecture can be a mix of EECs, SECs, PECs.
For now, focus is on achieving frequency synchronization
In the future phase and time of day will be specified
We already saw use case 1 and 2a where the legacy tdm service can be used to support frequency synchronization using SEC
We already say use case 1b where, with CES and ACR, frequency synchronization can be supported by MEN Operator
This ACR method is shown in the far right (grey) with TDM demarcation.
When the network migrates to supporting Ethernet demarcation then EECs or PECs can be used.
Key observation: The performance of the distribution architecture is measured by Interface Limits – Jitter/Wander.
Also, This Ethernet interface at the UNI needs to have additional capability – what?

## Slide 33: Summary
Ethernet has been adopted: there are new challenges
MEF providing solution for optimization
  4G/LTE
  Carrier Ethernet with Multiple Class of Service
  Synchronization
Total impact of new MEF work
  Efficient, profitable and scalable deployment for Mobile Operators Access Providers

## Slide 34: Addendum: Migration from TDM
Carrier Ethernet Network
UNI
RAN BS
RAN NC
UNI
UNI
Although Migration to Ethernet has now been mostly complete, the following slides are retained for completion

## Slide 35: Use Case: Migration to 3G with Ethernet
Mobile Operator operates 2G and 3G mobile networks
RAN Base Station Sites with both 2G and 3G radios
Frequency synchronization required – assume no GPS
Mobile Operator has TDM leased Lines between BS and NC sites
Legacy Network
TDM Leased Line (1.5 / 2 Mbps)
3G
2G
2G + 3G
2G + 3G
2G + 3G
BSC
RNC
Migration 1: Growth in Data (IP) Traffic
Migration 2: Need scalable Backhaul
Notes: Explain existing configuration of 2G and 3G Radio networks at RAN BS sites
Explain existing TDM leased Lines for 2G networks but also used for 3G traffic
Migration:
- BS and NC equipment for 3G is migrating to support Ethernet interfaces for IP traffic
Explosion in traffic is forcing Mobile Operator to seek scalable backhaul bandwidth

## Slide 36: Migration to 3G with Ethernet: Challenges
Problem:
  Capacity increase not cost-effective on TDM Leased Lines
Requirements
  Standard Services
  Manageability
  Reliability
  Quality of Service
  Synchronization
Solution:
  Carrier Ethernet Network
  MEF 8 and 6.x Services
Notes: A bit more detail on the approach to solving the challenges – Problem and Requirements
Emphasize that the solution is consistent with the Carrier Ethernet Attributes.
- solution (MEF 8 and MEF 6.x services)

## Slide 37: Mobile Backhaul for 2G Legacy RAN
Use Case 1b:
RAN CEs with TDM interfaces
All traffic with CES across MEN
Use Case 1a:
RAN CEs with TDM interfaces
Packet offload with CES
Frequency Synchronization can be with TDM Physical method
Frequency Synchronization can be with ACR/Packet method
Notes: Explain the following:
Mobile Operator may want to
  continue to use TDM services over legacy network for high priority voice and data
  Seek to scale backhaul for high growth data traffic but constrained with TDM interface at BS and NC
SP can provide CES to support low priority Packet offload with CES across a MEN/CEN
  Clarify that the model is like when a ‘TDM transport group’ gets an Ethernet service from the ‘data group’
Clarify that the Mobile Operator could also own the GIWF and just request Ethernet service from MEN/SP. This is not shown here.
Over time, Mobile Operator can migrate all traffic to use CES, if needed.
Important to note that SP can
  continue to use legacy TDM service to provide a network clock to BS.
  Else, can also use ACR of frame arrival in emulated service

## Slide 38: MEF EVC Services to support CES
2G
2G
2G
2G
E-Line_1
E-Line_2
E-Line_3
E-Line_4
Carrier Ethernet
Network
BSC
GIWF helps map legacy circuits
ELINE (EPL) between GIWFs
  CIR>0, CBS>0 & EIR = 0, EBS=0 for guaranteed bit rate
  Service Level Specification (SLS) in Service Level Agreement (SLA)
    Frame Delay, Frame Delay Range, Frame Loss Ratio, Availability
RNC
Generic Interworking Function (GIWF)
CEN Operator to design network to match service requirements
Frequency Synchronization
Interface Limits (Jitter/Wander) at UNI
Notes: Explain with bit more detail about the EVC, ie.,
Guaranteed bit rate and so EIR=0 and EBS=0 but CIR/CBS values suitable for emulated circuit (including overhead)
Also, EVC with performance to match emulated circuit requirements
  Example, low frame delay (FD), low inter frame delay variation (IFDV), high availability, etc.
Explain figure as a representative example of pt-pt EVCs (E-Line) between GIWFs for legacy 2G BS/BSC.
  Port based service (EPL)
Conclude: MEF Services have the right set of attributes to help the Mobile Operator to transition from TDM to Ethernet based Mobile Backhaul with SLAs to meet both legacy TDM and Ethernet services.

## Slide 39: Ethernet RAN Mobile Backhaul Migration
Use Case 2a
RAN CEs with TDM and Ethernet Interfaces
Use Case 2b
RAN CEs with Ethernet Interfaces
Frequency Synchronization can be with TDM service
Frequency Synchronization service from the MEN
Notes: With transition to 3G/LTE – RAN CEs are getting Ethernet interfaces
With MEF Compliant UNIs the Mobile Operator can get a MEF 6 (EVC based) service from the SP/MEN.
In some cases the Mobile Operator can continue to use the combination of legacy and MEF 6 services if the RAN CE support both TDM and Ethernet interfaces
Important to note: in use case 2a, the mobile operator can get network synchronization delivered via the legacy TDM connection.
In use case 2b alternate methods of synchronization distribution are needed.

## Slide 40: MEF Services for 3G RAN CEs
2G + 3G
2G + 3G
3G
2G + 3G
E-Line_1
E-Line_2
E-Line_3
E-Line_4
Carrier Ethernet
Network
BSC
Generic Interworking Function (GIWF)
UNI
Mobile Operator has MEF Compliant UNIs on RAN CEs
MEN Operator (as Service Provider) has MEF Compliant UNIs
  MEF Compliant UNIs for MEF Compliant MEF 6.x services
  1 or more Class of Service (CoS), e.g.. 3 CoS
  Service Level Specification (SLS) in Service Level Agreement (SLA)
E-LAN
2G
3G
UNI
RNC
Notes: Emphasize the need for
All MEF 6.x services: ELINE/E-Lan/E-Tree
Multiple Classes of Service: at least 2 – Real time vs Best Effort
SLS objectives to guarantee performance unique to each CoS instance
Also, critical to have MEF compliant UNIs
Remind again that frequency synchronization can be with ACR using frame arrival rates

## Slide 41
Thank you!
For MEF presentations please visit: http://www.metroethernetforum.org
Please visit www.metroethernetforum.org and www.ethernetacademy.net