## Slide 1: Introducing the Specifications of the MEF
MEF 22.1.1: Mobile Backhaul Phase 2
Amendment 1 - Small Cells

## Slide 2: MEF Reference Presentations
Intention
  These MEF reference presentations are intended to give general overviews of the MEF work and have been approved by the MEF Marketing Committee
  Further details on the topic are to be found in related specifications, technical overviews, white papers in the MEF public site Information Center: http://metroethernetforum.org/InformationCenter
  Notice
  © The Metro Ethernet Forum 2015. Any reproduction of this document, or any portion thereof, shall contain the following statement: "Reproduced with permission of the Metro Ethernet Forum." No user of this document is authorized to modify any of the information contained herein.

## Slide 3: Topics
Approved MEF Specifications
Introduction
Small Cell Background
MEF On-Going Work
Small Cell Radio Coordination
MEF 22.1.1 amendment
Summary

## Slide 4: Approved MEF Specifications*
Specification | Description
MEF 2 | Requirements and Framework for Ethernet Service Protection
MEF 3 | Circuit Emulation Service Definitions, Framework and Requirements in Metro Ethernet Networks
MEF 4 | Metro Ethernet Network Architecture Framework Part 1: Generic Framework
MEF 6.1 | Metro Ethernet Services Definitions Phase 2
MEF 7.1 | EMS-NMS Information Model Phase 2
MEF 8 | Implementation Agreement for the Emulation of PDH Circuits over Metro Ethernet Networks
MEF 9 | Abstract Test Suite for Ethernet Services at the UNI
MEF 10.2 | Ethernet Services Attributes Phase 2
MEF 11 | User Network Interface (UNI) Requirements and Framework
MEF 12.1 | Metro Ethernet Network Architecture Framework Part 2: Ethernet Services Layer
MEF 13 | User Network Interface (UNI) Type 1 Implementation Agreement
MEF 14 | Abstract Test Suite for Traffic Management Phase 1
MEF 15 | Requirements for Management of Metro Ethernet Phase 1 Network Elements
MEF 16 | Ethernet Local Management Interface
*Current at time of publication. See MEF web site for official current list, minor updates and superseded work (such as MEF 1 and MEF 5)

## Slide 5: Approved MEF Specifications
Specification | Description
MEF 17 | Service OAM Framework and Requirements
MEF 18 | Abstract Test Suite for Circuit Emulation Services
MEF 19 | Abstract Test Suite for UNI Type 1
MEF 20 | User Network Interface (UNI) Type 2 Implementation Agreement
MEF 21 | Abstract Test Suite for UNI Type 2 Part 1: Link OAM
MEF 22.1 | Mobile Backhaul Implementation Agreement Phase 2
MEF 22.1.1 | Amendment to MEF 22.1 – Small Cell Backhaul
MEF 23.1 | Class of Service Implementation Agreement Phase 2
MEF 24 | Abstract Test Suite for UNI Type 2 Part 2: E-LMI
MEF 25 | Abstract Test Suite for UNI Type 2 Part 3: Service OAM
MEF 26.1 | External Network Network Interface (ENNI) – Phase 2
MEF 27 | Abstract Test Suite For UNI Type 2 Part 5: Enhanced UNI Attributes & Part 6: L2CP Handling
MEF 28 | External Network Network Interface (ENNI) Support for UNI Tunnel Access and Virtual UNI
MEF 29 | Ethernet Services Constructs

## Slide 6: Approved MEF Specifications
Specification | Description
MEF 30 | Service OAM Fault Management Implementation Agreement
MEF 31 | Service OAM Fault Management Definition of Managed Objects
MEF 32 | Requirements for Service Protection Across External Interfaces
MEF 33 | Ethernet Access Services Definition
MEF 34 | Abstract Test Suite for Ethernet Access Services
MEF 35 | Service OAM Performance Monitoring Implementation Agreement
MEF 36 | Service OAM SNMP MIB for Performance Monitoring
MEF 37 | Abstract Test Suite for ENNI
MEF 38 | Service OAM Fault Management YANG Modules Technical Specification
MEF 39 | Service OAM Performance Monitoring YANG Modules Technical Specifications
MEF 40 | UNI and EVC Definition of Managed Objects Technical Specification
MEF 41 | Generic Token Bucket Algorithm Technical Specification
MEF 42 | ENNI and OVC Definition of Managed Objects Technical Specification
MEF 43 | Virtual NID (vNID) Functionality for E-Access Services Technical Specification
MEF 44 | Virtual NID (vNID) Definition of Managed Objects Technical Specification
MEF 45 | Multi-CEN L2CP Technical Specification

## Slide 7: Approved MEF Specifications
Specification | Description
MEF 46 | Latching Loopback Protocol and Functionality Technical Specification
MEF 47 | Carrier Ethernet Services for Cloud Implementation Agreement
MEF 48 | Service Activation Testing Technical Specification
MEF 49 | Service Activation Testing Control Protocol and PDU Formats Technical Specification
MEF 50 | Carrier Ethernet Service Lifecycle Process Model Guidelines Document

## Slide 8: This Overview Presentation
Purpose:
  This presentation is an introduction to MEF 22.1.1
Scope of the Amendment
  Mobile backhaul and midhaul, for macro and small cells, for mobile technologies
Audience
  Equipment manufacturers building devices that will carry mobile backhaul traffic over Carrier Ethernet
  Useful for mobile backhaul service providers architecting their systems for Carrier Ethernet
  For wire-line service providers architecting their systems for the inclusion of mobile backhaul traffic over Carrier Ethernet

## Slide 9: MEF 22.1.1 and Relationship to other SDOs
Industry trends
Other SDOs
MEFs own work as the foundation
Standardized
reference
points
Service
Requirements
(Service Types,
CoS, Eth OAM, etc)
Synchronization
Recommendations
MEF 10.2
MEF 6.1
MEF 13
MEF 23.1
3G to 4G/LTE
TR.221
MEF 22.1.1
Capacity/ Coverage
Small Cells Amendment

## Slide 10: MEF Mobile Backhaul: Work in Progress
MEF-22.2
  Mobile backhaul across multiple service providers’ networks using ENNI/OVC based services
  Alignment with MEF 6.2 & MEF 10.3
MEF-22.2.1
  Time/Phase Synchronization support

## Slide 11: Small Cell Background

## Slide 12: End User Experience Challenges
Increase overall cell site performance
Increase cell edge data rates
Increase indoor data rates
Data rate
3
1
2
3
2
Notes: 12

## Slide 13: Increase Capacity & Coverage
Data rate
’Super-macro’
Micro & Pico
’Super-macro’
3
1
2
3
3
”Super-macro” – advanced antennas, spectrum aggregation
Macro densification
Small cells – Micro & Pico
Notes: 13

## Slide 14: Increasing Network Capacity with Small Cells
Target capacity per cell | 100 to 300 Mbps | 25 to 100 Mbps
Cell density relative to macrocell | 1 | 5 to 25
Total capacity | 100 to 300 Mbps | 125 Mbps to 2.5 Gbps
Indoor coverage | Poor | Good
Impact of SON / coordination | Low | High
Macro Cell Small Cell
Network
Transformation
Small cells are best to meet the demand challenge

## Slide 15: Heterogeneous Network
Required Capacity
Small cells
Macro densification
Current Capacity
Improved macros

## Slide 16: Heterogeneous Network Deployment
Improved macros
Macro densification
Small cells
Improved macros
Dense urban
Urban
Suburban
Rural
Improved macros
Macro densification
Area traffic density
Small Cells advantage is greater in Metropolitan Areas but also in other areas to increase coverage and/or capacity

## Slide 17: Small Cell Coordination

## Slide 18: Small Cells & Radio Coordination
To improve uplink coverage
  i.e. cell edge throughput
To increase capacity
  Capacity improves as coverage improves
Offload congested macro cells
Why is Radio coordination needed?
  Interference coordination between macro and small cells will Boost coverage and capacity
Small cells improves coverage and capacity

## Slide 19: What is Coordination?
Multiple schemes and possibilities, often used in combination
  Coordinated scheduling
  Coordinated beamforming (null forming)
  Dynamic point selection
  Joint transmission/reception
Macro (high power)
Small cell (low power)
Best downlink
Best uplink
Best uplink
Best downlink
Notes: NRJ-12:007724 Uen, Rev PA1
19
19

## Slide 20: What is CoMP?
Coordinated MultiPoint
Multiple schemes and possibilities, often used in combination
  Coordinated scheduling
  Coordinated beamforming (null forming)
  Dynamic point selection
  Joint transmission/reception
  …
Null forming
different resources scheduled
Notes: NRJ-12:007724 Uen, Rev PA1
20
20

## Slide 21: Where are the CoMP gains?
No CoMP Gain
CoMP Bandwidth Gain: Uplink ~30-50%, Downlink ~15%
CoMP Bandwidth Gain: Uplink ~50-100%, Downlink ~30%
The majority of the uplink/downlink bandwidth gain is on the cell edge between the small cell and the macro it shares a footprint with

## Slide 22: Different Degrees of Macro Cell Coordination
Moderate coordination
  Example: Coordinated deployment of pico cell in a macro network using range expansion or eICIC (enhanced Inter-Cell Interference Coordination)
Very tight coordination
  Example: DU/RU radio network using features such as joint scheduling (air interface) over CPRI (Common Public Radio Interface)
No coordination
  Example: uncoordinated deployment with femto cell in a macro network
Tight coordination
  Example: Coordinated deployment of pico cell in a macro network using features such as coordinated scheduling

## Slide 23: eICIC - Moderate Coordination
Macro cell avoids scheduling in “protected” subframes
  Capacity loss in macro layer and pico layer
  Reduced interference from macro cell in “protected” subframes
Advanced Rx in Ue required for range expansion
Cell size: Dense urban environment
Time alignment: +/- 5us required between macro and small cell
Latency: No special demands
Bandwidth Needs: Low
UEs in range expansion zone scheduled in protected subframes only
UEs in inner part of pico cell scheduled in any subframe
UEs in macro cell scheduled in non-protected subframes only
Protected subframes
Unprotected subframes
Time alignment is needed
Notes: SBM LTE R&R WS 121010 Hetnet
15-05-26
NRJ-12:007724 Uen, Rev PA1
23

## Slide 24: DL Coordination Scheduling - Tight Coordination
Down Link
Share information.
Based on received information, perform coordinated scheduling
Cell size: Dense urban environment
Time alignment: +/-1.5us required between macro and small cell
Latency: 1..10ms – the lower the latency, the better the cell edge gain
Bandwidth: Up to 20Mbps, per coordinated cell pair
Coordinating link
Time alignment and low latency is needed
Notes: NRJ-12:007724 Uen, Rev PA1
24

## Slide 25: UL Joint Reception - Very Tight Coordination
TIME ALIGNMENT, HIGH BW & VERY LOW LATENCY => BASEBAND INTERNAL ONLY
Up Link - Schedule UEs.
Receive transmitted data.
Share received data and jointly process it
(Communicate back ACK/NACK to BS responsible to certain UE.)
Cell size: Dense urban environment
Time alignment: +/-1.5us required between cells
Latency: <0.5ms one way
Bandwidth: 1Gbps per antenna,
internal RBS interface
CPRI
CPRI
Common baseband
S1/X2
Radio Unit
Radio Unit
Time alignment, high bandwidth &very low latency is needed
Notes: NRJ-12:007724 Uen, Rev PA1
25

## Slide 26: MEF 22.1.1 - Small Cells

## Slide 27: Introduction to the Amendment
The MEF 22.1.1 amendment makes the following changes to MEF 22.1:
  Backhaul, Midhaul and Fronthaul are defined
  Small Cells, along with heterogeneous networks and radio coordination, are introduced
  New variations of existing use cases
  new use case 3 is defined for the midhaul case
  CPOs for small cells with tight radio coordination are described
  CPOs for small cells with split bearer are described
  A new Appendix defines the Aggregation Node
  A new Appendix summarizes LTE radio coordination

## Slide 28: MEF 22.1.1 – New Terminology
Remote radio site
RRU
Basstation site
Marco RBS
Network controller / gateway site
SGW, MME
Small cell site
Small RBS
Fronthaul
Backhaul
Midhaul
Backhaul
Backhaul – macro/small cell to core
Midhaul – small cell to macro
Fronthaul – remote radio to baseband unit

## Slide 29: Small Cell alternatives
Distributed Baseband Architecture
- Backhaul – macro or small cell BS to core
- Midhaul – small cell to macro
Common Baseband Architecture
– Backhaul – macro BS to core
– Fronthaul - CPRI interconnect between remote radio units and baseband unit
CPRI
CPRI
S1/X2
S1/X2
S1/X2
S1/X2
SmallRBS
SmallRBS
mRRU
mRRU
Small cells are operator-controlled, low-powered radio access nodes, which typically have a range from 10 metres to several hundred metres.
They may be a complete basestation (distributed as on the left) or just the radio/antenna (common as on the right)
Notes: SBM LTE R&R WS 121010 Hetnet
15-05-26
NRJ-12:007724 Uen, Rev PA1
29
15-05-262011-10-19
29
metroPCS

## Slide 30: Generalized BS aggregation
CSAG
LTE
RAN BS site
UNI
UNI
CEN
EVC
UNI-C
UNI-C
UNI-N
UNI-N
Small cell site
LTE
CDMA
GSM
LTE
LTE
Mobile Operator A
Mobile Operator B
Legend
CSAG- Cell Site Aggregation Gateway
CSAG may be used by the mobile operator to
aggregate backhaul traffic before the MEF UNI.
The aggregation may be L2 or L3

## Slide 31: CEN and non-CEN hybrid
Mobile Network RAN NC site
UNI
UNI
CEN
EVC
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Mobile Network RAN BS site
UNI
UNI
CEN
EVC
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Non-MEF service
e.g., IP
MEF MBH can be part of a multi-technology end-to-end backhaul

## Slide 32: Backhaul with Small Cell Extension Use Cases
Mobile Network RAN BS site
Mobile Network RAN NC site
UNI
UNI
CEN
EVC(m)
RAN CE
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Small Cell RAN BS site
UNI
UNI
CEN
EVC(s)
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
S1
Backhaul
Midhaul
Mobile Network RAN BS site
Mobile Network RAN NC site
UNI
UNI
CEN
EVC(m)
RAN CE
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Small Cell RAN BS site
UNI
UNI
CEN
EVC(s)
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
S1
X2
Backhaul
Midhaul
LTE S1 Backhaul:
LTE S1 & X2 Backhaul:

## Slide 33: Backhaul with Small Cell Extension Use Cases (2)
Mobile Network RAN BS site
Mobile Network RAN NC site
UNI
UNI
CEN
EVC(m)
RAN CE
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Small Cell RRU site
Fibre or DWDM
S1
CPRI
Backhaul
Fronthaul
Mobile Network RAN BS site
Mobile Network RAN NC site
UNI
UNI
CEN
EVC(m)
RAN CE
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Small Cell RAN BS site
UNI
UNI
CEN
EVC(s)
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
S1
X2+
Backhaul
Midhaul
LTE-A Dual Connectivity :
CPRI & Backhaul:

## Slide 34: Transport Requirements
Backhaul
  Macro – Core (eNB – EPC)
  Packet based
Fronthaul
  Baseband – Radio Unit (Main-Remote)
  Dedicated Fibre
Midhaul
  Macro – small cell (eNB-eNB)
  Options
    Same as backhaul
    Support tight coordination
    Support X2+
Latency ~20ms
Latency ~50us
Latency ~20ms
Latency ~1ms
Latency ~50ms

## Slide 35: New CPO for tight coordination
Constrained PT1 : FD of 1ms (CoS Name H) – 10ms (CoS Name L)
PT1 M – 20ms
PT1C M – 5 ms
Site – 1ms
Node – 1 ms
E2E budget example for S1: 1+5+1+20=27ms for CoS Name M

## Slide 36: Summary
The need for greater capacity, indoor penetration and spectral-reuse is driving the requirement for small cell solutions
Small cell networks present their own unique deployment and backhaul challenges
MEF-22.1.1 will cover Small cell with tight coordination backhaul and is backwards compatible with MEF-22.1