## Slide 1: Introducing the Specifications of the MEF
MEF 38: Service OAM Fault Management YANG Modules Technical Specification
April 2012

## Slide 2: MEF Reference Presentations
Intention
  These MEF reference presentations are intended to give general overviews of the MEF work and have been approved by the MEF Marketing Committee
  Further details on the topic are to be found in related specifications, technical overviews, white papers in the MEF public site Information Center: http://metroethernetforum.org/InformationCenter
  Notice
  © The Metro Ethernet Forum 2012. Any reproduction of this document, or any portion thereof, shall contain the following statement: "Reproduced with permission of the Metro Ethernet Forum." No user of this document is authorized to modify any of the information contained herein.

## Slide 3: Outline
Approved MEF Specifications
This presentation
About this Specification
In Scope / Out of Scope
Terminology, Concepts & Relationship to other standards
Section Review
  Major topics
    Minor topics
Examples/Use Cases
Summary

## Slide 4: Approved MEF Specifications*
Specification | Description
MEF 2 | Requirements and Framework for Ethernet Service Protection
MEF 3 | Circuit Emulation Service Definitions, Framework and Requirements in Metro Ethernet Networks
MEF 4 | Metro Ethernet Network Architecture Framework Part 1: Generic Framework
MEF 6.1 | Metro Ethernet Services Definitions Phase 2
MEF 7.1 | EMS-NMS Information Model Phase 2
MEF 8 | Implementation Agreement for the Emulation of PDH Circuits over Metro Ethernet Networks
MEF 9 | Abstract Test Suite for Ethernet Services at the UNI
MEF 10.2 | Ethernet Services Attributes Phase 2
MEF 11 | User Network Interface (UNI) Requirements and Framework
MEF 12.1 | Metro Ethernet Network Architecture Framework Part 2: Ethernet Services Layer
MEF 13 | User Network Interface (UNI) Type 1 Implementation Agreement
MEF 14 | Abstract Test Suite for Traffic Management Phase 1
MEF 15 | Requirements for Management of Metro Ethernet Phase 1 Network Elements
MEF 16 | Ethernet Local Management Interface
*Current at time of publication. See MEF web site for official current list, minor updates and superseded work (such as MEF 1 and MEF 5)

## Slide 5: Approved MEF Specifications
Specification | Description
MEF 17 | Service OAM Framework and Requirements
MEF 18 | Abstract Test Suite for Circuit Emulation Services
MEF 19 | Abstract Test Suite for UNI Type 1
MEF 20 | User Network Interface (UNI) Type 2 Implementation Agreement
MEF 21 | Abstract Test Suite for UNI Type 2 Part 1: Link OAM
MEF 22.1 | Mobile Backhaul Implementation Agreement Phase 2
MEF 23.1 | Class of Service Implementation Agreement Phase 2
MEF 24 | Abstract Test Suite for UNI Type 2 Part 2: E-LMI
MEF 25 | Abstract Test Suite for UNI Type 2 Part 3: Service OAM
MEF 26.1 | External Network Network Interface (ENNI) – Phase 2
MEF 27 | Abstract Test Suite For UNI Type 2 Part 5: Enhanced UNI Attributes & Part 6: L2CP Handling
MEF 28 | External Network Network Interface (ENNI) Support for UNI Tunnel Access and Virtual UNI
MEF 29 | Ethernet Services Constructs

## Slide 6: Approved MEF Specifications
Specification | Description
MEF 30 | Service OAM Fault Management Implementation Agreement
MEF 31 | Service OAM Fault Management Definition of Managed Objects
MEF 32 | Requirements for Service Protection Across External Interfaces
MEF 33 | Ethernet Access Services Definition
MEF 34 | Abstract Test Suite for Ethernet Access Services
MEF 35 | Service OAM Performance Monitoring Implementation Agreement
MEF 36 | Service OAM SNMP MIB for Performance Monitoring
MEF 37 | Abstract Test Suite for ENNI
MEF 38 | Service OAM Fault Management YANG Modules Technical Specification
MEF 39 | Service OAM Performance Monitoring YANG Modules Technical Specifications

## Slide 7: MEF 38 Specification Overview
Standardized Services
Purpose
An Implementation Agreement (IA) which provides for Service Operations, Administration, and Maintenance (SOAM) that satisfies and extends the Performance Monitoring (PM) framework and requirements described in MEF 17.
Audience
All, since it provides the fundamentals required to deliver Carrier Ethernet services.
Service OAM Fault Management YANG Modules Technical Spec
MEF 38

## Slide 8: MEF Specification Overview
Standardized Services
Purpose
Specifies the Fault Management (FM) YANG Modules necessary to implement Service Operations, Administration, and Maintenance (OAM) that satisfies the Service OAM requirements and framework specified by MEF 17, MEF 30, the management objects specified in MEF 7.1, MEF 31, and the FM functions defined in IEEE 802.1Q and ITU-T Y.1731.
Audience
Applicable to entire Metro Ethernet Market including Service Providers, Access Providers, equipment vendors, and EMS/NMS/OSS vendors to provision and monitor equipment that is MEF compatible.
MEF 38 - Service OAM Fault Management YANG Modules Technical Specification

## Slide 9: Overview of MEF 38

## Slide 10: About MEF 38
Purpose:
  This presentation is an introduction to MEF 38 - Service OAM Fault Management YANG Modules
Audience
  Equipment Manufacturers building devices that will carry Carrier Ethernet Services
  Service Providers delivering Carrier Ethernet Services
  EMS/NMS/OSS tool vendors developing back office applications for managing Carrier Ethernet Services
Other Documents
  Presentations of other MEF specifications and an overview of all specifications is available on the MEF web site
  Other materials such as white papers and case studies are also available

## Slide 11: Service OAM
MEF 17 provides the framework
  Relevant for Subscribers (customers), Operators and Service Providers
Fault Management IA (MEF 30)
  FM of MEF Services
  Specifies profile of protocols defined in IEEE 802.1Q and ITU-T Y.1731
  Provides basic SOAM architecture and requirements for each of the recommended MEGs
Performance Management IA (MEF 35)
  PM of MEF Services
  Specifies profile of protocols defined in ITU-T Y.1731
MEF 31 & MEF 36
  SNMP MIBs (Definition of Management Objects) for FM (MEF 31) and PM (MEF 36)
  Provides data models for SNMP-based network management

## Slide 12: MEF 38 - In Scope/Out of Scope
MEF 38 requirements are primarily driven by MEF 30 and leverage the OAM functions & managed objects defined by MEF 31, IEEE 802.1Q and ITU-T Y.1731
Managed objects to perform Fault Management functions such as Continuity Check, Loopback and Link Trace are covered in this Technical Specification
SOAM Performance Management capabilities are covered in MEF 39

## Slide 13: Terminology and Concepts
MEF 38 adheres to MEF 30 terminology:
  Refer to MEF 30 for ME, MEG, MEP, MIP, MEG Level, MEG CoS
  Continuity Check Message (CCM)
  Alarm Indication Signal (AIS)
  Remote Defect Indication (RDI)
MEF 38 introduces protocol specific terminology
  Network Configuration Protocol (NETCONF)
  NETCONF Client/Server
  YANG Data Modeling Language and Modules
  Element/Network Management System (EMS/NMS)
  Operations Support System (OSS)
  Remote Procedure Call (RPC)
  Extensible Markup Language (XML)
  Secure Shell (SSH)
MEF-30 aligns with terminology found in ITU Y.1731

## Slide 14: Relationship with other Specifications

## Slide 15: MEF Service Lifecycle and SOAM
Network Management
Fault management is a critical part of a circuit’s lifecycle

## Slide 16: MEF Specification Section Review

## Slide 17: Introducing MEF 38
The presentation is broken into sections:
  Overview
  Network Management Concepts/Topologies
  Initial Configuration
  OAM Functions
    Configuration
    Status
  Summary
  Where to find additional information

## Slide 18: Overview of NETCONF
NETCONF is an IETF network management protocol designed to manage configuration:
  Distinction between configuration and state data
  Multiple configuration data stores:
    Candidate, running, startup
  Configuration change validations
  Configuration change transactions
  Selective data retrieval with filtering
  Extensible Remote Procedure Call (RPC) mechanism

## Slide 19: Overview of YANG
YANG is a data modeling language for NETCONF:
  Human readable, and easy to learn representation
  Hierarchical configuration data models
  Reusable types and groupings (structured types)
  Extensibility through augmentation mechanisms
  Supports definition of operations (RPCs)
  Formal constraints for configuration validation
  Data modularity through modules and sub-modules
  Well defined versioning rules

## Slide 20: Why Not SNMP for Configuration?
Feature | Drawback
Stateless, connectionless, single attribute get and set | Not practical for complex, multi-device configuration changes
No difference between configuration and state data | No support for backup and restore
Data-centric (table-driven) view of the world | Semantic mismatch with task-oriented world of configuration
NETCONF specifically not meant to replace SNMP in general but to significantly improve in the area of configuration management

## Slide 21: Management Framework
IEEE 802.1ag End-to-End Connectivity Fault Management
ITU-T Y.1731 End-to-End Performance Monitoring
Service OAM
NETCONF 4-Layer Model

## Slide 22: SOAM CFM YANG Module Overview
Connectivity Fault Management module describes IEEE 802.1Q and 802.1ap by implementing the objects and fuctions
  Provides all managed objects which are defined in the corresponding SNMP MIB Modules:
    IEEE8021-CFM-MIB
    IEEE8021-CFM-V2-MIB
    IEEE8021-TC-MIB
Provides top level structure of Ethernet CFM
  MD, MA, MEP

## Slide 23: SOAM FM YANG Module Overview
Fault Management module describes SOAM FM (MEF 30) by implementing the objects and fuctions
  Provides all managed objects which are defined in the corresponding SNMP MIB Modules (MEF 31):
    MEF-SOAM-FM-MIB
    MEF-SOAM-TC-MIB
Provides extensions to IEEE
  CC, LB, LT, AIS, LCK, Test

## Slide 24: YANG Module Details

## Slide 25: mef-cfm.yang Module Details
The next several slides highlight the data model hierarchy of the mef-cfg.yang module.
Refer to the specification for node descriptions
Container: default-md-levels
  Leaf: md-level
  Leaf: mhf-creation
  Leaf: default-id-permission
  List: default-md-level
    Leaf: primary-vid (key)
    Leaf: component-id (key)
    Leaflist: vid
    Leaf: status
    Leaf: md-level
    Leaf: mhf-creation
    Leaf: default-id-permission

## Slide 26: mef-cfm.yang Module Details
List: configuration-error-list
  Leaf: vlan-identifier (key)
  Leaf: interface (key)
  Leaf: error-conditions
List: maintenance-domain
  Leaf: id (key)
  Leaf: name-type
  Leaf: name
  Leaf: md-level
  Leaf: mhf-creation
  Leaf: id-permission

## Slide 27: mef-cfm.yang Module Details
  List: maintenance-association
    Leaf: id (key)
    Leaf: name-type
    Leaf: name
    List: component-list
      Leaf: component-id (key)
      Leaflist: vid
      Leaf: mhf-creation
      Leaf: id-permission
    Leaf: ccm-interval
    Leaflist: remote-meps
    List: maintenance-association-end-point
      Leaf: mep-identifier (key)

## Slide 28: mef-cfm.yang Module Details
      Leaf: interface
      Leaf: direction
      Leaf: primary-vid
      Leaf: administrative-state
      Leaf: mac-address
      Leaf: ccm-ltm-priority
      Container: continuity-check
        Leaf: cci-enabled
        Leaf: fng-state
        Leaf: lowest-fault-priority-defect
        Leaf: highest-priority-defect-found
        Leaf: fng-alarm-time
        Leaf: fng-reset-time
        Leaf: active-defects

## Slide 29: mef-cfm.yang Module Details
        Leaf: last-error-ccm
        Leaf: last-cross-connect-ccm
        Leaf: ccm-sequence-error-count
        Leaf: sent-ccms
      Container: loopback
        Leaf: replies-received
        Leaf: replies-transmitted
        Leaf: out-of-order-replies-received
        Leaf: bad-msdu
      Container: linktrace
        Leaf: unexpected-replies-received
        Container: linktrace-database
          List: linktrace
            Leaf: transaction-id (key)

## Slide 30: mef-cfm.yang Module Details
            Container: target-address
              Choice: address-type
                Leaf: mac-address
                Leaf: mep-id
            Leaf: transmit-ltm-flags
            Leaf: default-ttl
            List: reply
              Leaf: reply-order (key)
              Leaf: reply-ttl
              Leaf: forwarded
              Leaf: terminal-mep
              Leaf: last-egress-identifier
              Leaf: next-egress-identifier
              Leaf: ltr-relay

## Slide 31: mef-cfm.yang Module Details
              Choice: chassis-id-subtype
                Leaf: chassis-component
                Leaf: interface-alias
                Leaf: port-component
                Leaf: mac-address-type
                Leaf: network-address
                Leaf: interface-name
                Leaf: local
              Container: management-address
                Choice: management-address
                <series of case statements>
              Leaf: ingress-action
              Leaf: ingress-mac
              Container: ingress-port-id

## Slide 32: mef-cfm.yang Module Details
                Choice: port-id-subtype
                Leaf: interface-alias
                Leaf: port-component
                Leaf: mac-address
                Leaf: network-address
                Leaf: interface-name
                Leaf: agent-circuit-id
                Leaf: local
              Leaf: egress-action
              Leaf: egress-mac
              Container: egress-port-id
                Choice: port-id-subtype (see above)
              Leaf: organization-specific-tlv

## Slide 33: mef-cfm.yang Module Details
      Container: remote-mep-database
        List: remote-mep
          Leaf: remote-mep-id (key)
          Leaf: remote-mep-state
          Leaf: failed-ok-time
          Leaf: mac-address
          Leaf: rdi
          Leaf: port-status-tlv
          Leaf: interface-status-tlv
          Choice: chassis-id-subtype (see above)

## Slide 34: mef-cfm.yang Module Details
RPC: transmit-loopback
  Inputs: mep-id, target-address, number-of-messages, data-tlv, vlan-priority, vlan-drop-eligible
  Outputs: none
RPC: abort-loopback
  Inputs: mep-id
  Outputs: none
RPC: transmit-linktrace
  Inputs: mep-id, target-address, transmit-ltm-flags, default-ttl
  Outputs: transaction-id

## Slide 35: mef-cfm.yang Module Details
Notification identifier: fault-alarm
  Container: alarm
    Leaf: mep-id
    Leaf: active-defects

## Slide 36: Summary

## Slide 37: Summary MEF 38
MEF 38 defines the managed objects specified with the YANG data modeling language for using the NETCONF network management interface for the MEF 30 Service OAM Fault Management protocol
MEF 38 enables MEF equipment providers to provide a standardized XML-based new generation management interface for the SOAM Fault Management functions:
  Continuity Check/Remote Defect Indication
  Loopback
  Linktrace
  Alarm Indication Signal
  Lock Signal
  Test Signal

## Slide 38: Related Specifications
MEF 30 SOAM FM
MEF 31 SOAM FM MIB
IEEE 802.1Q
ITU-T Y.1731
MEF 17 SOAM Requirements & Framework - Phase 1
MEF 12.1 CE Network Architecture Framework Part 2: ETH Service Layer – Base Elements
IETF RFC 6241 (NETCONF) & RFC 6020 (YANG)

## Slide 39: Final Word
Service OAM
  In the context of MEF 38, data models (YANG Modules) are defined that support service-level OAM in MENs
Next Actions (For Further Information)
  Read the full MEF 30 Fault Management Implementation Agreement specification
  Read the full MEF 38 specification (note, review of MEF 17, MEF 7.1, MEF 31 and MEF 15 may also be helpful)
  Understand the principal service OAM components and capabilities
Notes: This section goes into further detail in detailing the defined Service Attributes and parameters requirement and recommendations as specified for each of the defined services: EPL, EVPL and E-LAN.
(Refer to the Specs and the accompanying Ethernet Service Description document for more details)

## Slide 40: For Full Details …
Please visit www.metroethernetforum.org Select Information Center on Left Navigation to access the full specification and extracted YANG files
Carrier Ethernet Network
UNI
UNI
CE
CE
CE
Carrier Ethernet 2.0
EVPL Services
UNI
Carrier Ethernet 2.0
EVP-LAN Service
ISP POP
Internet
UNI
UNI
CE
CE
CE
UNI
Carrier Ethernet Network
EVC: Ethernet Virtual Connection
UNI: User Network Interface. the physical demarcation point between the responsibility of the Service Provider and the responsibility of the End-User/Subscriber
CE Customer Equipment
E-LAN Service type
E-Line Service type

## Slide 41: Accelerating Worldwide Adoption of Carrier-class Ethernet Networks and Services
www.MetroEthernetForum.org