## Slide 1: Introducing the Specifications of the MEF
MEF 7.2: Carrier Ethernet
Management Information Model
July 2013

## Slide 2: MEF Reference Presentations
Intention
  These MEF reference presentations are intended to give general overviews of the MEF work and have been approved by the MEF Marketing Committee
  Further details on the topic are to be found in related specifications, technical overviews, white papers in the MEF public site Information Center: http://metroethernetforum.org/InformationCenter
  Notice
  © The Metro Ethernet Forum 2013. Any reproduction of this document, or any portion thereof, shall contain the following statement: "Reproduced with permission of the Metro Ethernet Forum." No user of this document is authorized to modify any of the information contained herein.

## Slide 3: Outline
Approved MEF Specifications
Specification Overview
OAM Overview
Use Cases
Summary

## Slide 4: Approved MEF Specifications*
Specification | Description
MEF 2 | Requirements and Framework for Ethernet Service Protection
MEF 3 | Circuit Emulation Service Definitions, Framework and Requirements in Metro Ethernet Networks
MEF 4 | Metro Ethernet Network Architecture Framework Part 1: Generic Framework
MEF 6.1 | Metro Ethernet Services Definitions Phase 2
MEF 7.2 | Carrier Ethernet Management Information Model
MEF 8 | Implementation Agreement for the Emulation of PDH Circuits over Metro Ethernet Networks
MEF 9 | Abstract Test Suite for Ethernet Services at the UNI
MEF 10.2 | Ethernet Services Attributes Phase 2
MEF 11 | User Network Interface (UNI) Requirements and Framework
MEF 12.1 | Metro Ethernet Network Architecture Framework Part 2: Ethernet Services Layer
MEF 13 | User Network Interface (UNI) Type 1 Implementation Agreement
MEF 14 | Abstract Test Suite for Traffic Management Phase 1
MEF 15 | Requirements for Management of Metro Ethernet Phase 1 Network Elements
MEF 16 | Ethernet Local Management Interface
*Current at time of publication. See MEF web site for official current list, minor updates and superseded work (such as MEF 1 and MEF 5)

## Slide 5: Approved MEF Specifications
Specification | Description
MEF 17 | Service OAM Framework and Requirements
MEF 18 | Abstract Test Suite for Circuit Emulation Services
MEF 19 | Abstract Test Suite for UNI Type 1
MEF 20 | User Network Interface (UNI) Type 2 Implementation Agreement
MEF 21 | Abstract Test Suite for UNI Type 2 Part 1: Link OAM
MEF 22.1 | Mobile Backhaul Implementation Agreement Phase 2
MEF 23.1 | Class of Service Implementation Agreement Phase 2
MEF 24 | Abstract Test Suite for UNI Type 2 Part 2: E-LMI
MEF 25 | Abstract Test Suite for UNI Type 2 Part 3: Service OAM
MEF 26.1 | External Network Network Interface (ENNI) – Phase 2
MEF 27 | Abstract Test Suite For UNI Type 2 Part 5: Enhanced UNI Attributes & Part 6: L2CP Handling
MEF 28 | External Network Network Interface (ENNI) Support for UNI Tunnel Access and Virtual UNI
MEF 29 | Ethernet Services Constructs

## Slide 6: Approved MEF Specifications
Specification | Description
MEF 30.1 | Service OAM Fault Management Implementation Agreement: Phase 2
MEF 31 | Service OAM Fault Management Definition of Managed Objects
MEF 32 | Requirements for Service Protection Across External Interfaces
MEF 33 | Ethernet Access Services Definition
MEF 34 | Abstract Test Suite for Ethernet Access Services
MEF 35 | Service OAM Performance Monitoring Implementation Agreement
MEF 36 | Service OAM SNMP MIB for Performance Monitoring
MEF 37 | Abstract Test Suite for ENNI
MEF 38 | Service OAM Fault Management YANG Modules Technical Specification
MEF 39 | Service OAM Performance Monitoring YANG Modules Technical Specifications
MEF 40 | UNI and EVC Definition of Managed Objects
*Current at time of publication. See MEF web site for official current list, minor updates (such as MEF 31.0.1 amendment to this document) and superseded work (such as MEF 1 and MEF 5)

## Slide 7: MEF Specification Overview
Purpose
This Specification defines a common set of managed object definitions that are consistent and readily integrated into a Carrier Ethernet Provider’s operations environment. This common management model helps ensure that vendors provide management functionality and information in their OSSs, NMSs, EMSs, and NEs in a logically consistent fashion, and allows service providers to readily integrate such capabilities into their management environment..
Audience
Equipment Manufacturers building devices that will carry Carrier Ethernet Services
Useful for Service Providers architecting their systems and providing services.
Tool vendors for developing back office applications
MEF 7 - EMS-NMS Information Model Element Management System–Network Management System

## Slide 8: About MEF 7.2
Purpose:
  This presentation is an introduction to MEF 7.2 – Carrier Ethernet Management Information Model
Audience
  Equipment Manufacturers building devices that will carry Carrier Ethernet Services
  Service Providers delivering Carrier Ethernet Services
  EMS/NMS/OSS tool vendors developing back office applications for managing, provisioning and monitoring Carrier Ethernet Services
Other Documents
  Presentations of other MEF specifications and an overview of all specifications is available on the MEF web site
  Other materials such as white papers and case studies are also available

## Slide 9: EMS – NMS Information Model
A Specification
  Enable consistent definition of the management information required to manage Carrier Ethernet.
A Model
  Defines the specific EMS-NMS management interface and objects for each specific interface profile such as Common Object Request Broker Object (CORBA) IDL, Simple Network Management Protocol (SNMP), JAVA, XML, etc.
Scope
  Ethernet (ETH) layer UNI configuration provisioning
  ETH layer configuration and provisioning
  ETH layer network connection and fault management (including setup/modification, notification, testing)
  Ethernet External Network Network Interface (ENNI) Service Attributes
  UNI Tunnel Access (UTA) / Virtual User Network Interface (VUNI) Service Attributes
  SOAM Service Attributes
  Virtual Network Interface Device (vNID) Remote Management Interface
  Ethernet Access Services

## Slide 10: OAM Overview

## Slide 11: MEF Service OAM
MEF 7.2 defines a means to provide OAM at the Ethernet Services layer
  Does not define OAM at the transport link/ network layers
  Compliments/relies on the work done in the ITU, IEEE and IETF at the Transport data link and Network layers
Provides a frame work and concepts for managing and monitoring flows across a connectionless network
  From end to end
  From Operator to Operator
Provides mechanism to perform:
  Node Discovery, Establish connectivity, monitor CoS, and detect service impairments

## Slide 12: Key Assumptions behind MEF OAM
Assumes Ethernet is only common denominator
  For example: 802.3 Ethernet, Ethernet over SONET/SDH, RPR, etc.
  Must use Ethernet framing for OAM communications
Ethernet segments interconnected with forwarding entities (bridges, etc.)
  Connectionless (like IP)
  Segment can be real or virtual
Must measure “per service” and “fate share” with the data plane
  Out-of-band OAM not reflective of the data plane
  OAM mixes with user data within the core network
Small initial focus on “SLA” metrics
  Connectivity, latency, loss, jitter, availability
Other functions may follow later
  Traceroute, RDI/AIS, other
Domain oriented
  Domain may be intra-provider, inter-provider, customer-to-customer, etc.

## Slide 13: Network Layering Concepts
Flows, connections and resources can all be managed separately at each LND
Each can remain independent
Each in turn can pass information to upper management domains to isolate issues.
Layer Network Domains
(LND)
IP
ETH
MPLS
SONET/SDH
WDM

## Slide 14: Use Cases

## Slide 15: Carrier Ethernet Management
Management Interface includes Configuration, Fault, Performance, and Common functions

## Slide 16: Configuration Management (CM)
Provides the description of the various elements necessary for Configuration of Carrier Ethernet
A couple of Configuration Function examples are given in the following slides

## Slide 17: CM Example
The next slide provides an example of the detail contained in MEF 7.2
The figure shows the functions for Interface Management
The slide after that shows the text describing ENNI Creation
Each function is documented in manner displayed on the ENNI Creation Example slide

## Slide 18: CM Example – Interface Management
Create, Delete, Modify, Query functions defined for
  UNI
  VUNI
  ENNI
Flow Point Pool (FPP) Management

## Slide 19: ENNI Creation Example
Name | ETH Flow Point Pool (FPP) ENNI Creation
Summary | The Carrier Ethernet Manager creates and configures an ETH ENNI on a pre-selected port. ETH FPP ENNIs may be created automatically by Managed System when physical ports are created, and can be retrieved by Carrier Ethernet Manager.
Actor(s) | Carrier Ethernet Manager
Assumptions | The Carrier Ethernet Manager has the authority to create the ETH ENNI.
Pre-Conditions | The Carrier Ethernet Manager has established communication with Managed System.
Begins When | The Carrier Ethernet Manager has selected a port (e.g., Generic Transport TTP) and sends a request to provision an ETH_FPP_ENNI representing an Ethernet ENNI on the port.
Description | The Carrier Ethernet Manager needs to create a new ETH ENNI associated with a specific port. The Carrier Ethernet Manager requests the creation of a new Ethernet FPP ENNI to be managed by the Managed System. As part of the creation request, the Carrier Ethernet Manager provides Ethernet ENNI configuration parameters. Based on the creation request, the Managed System creates an instance of ETH FPP ENNI and returns the name of the new ETH FPP ENNI instance. In addition, an Object Creation Notification for the new instance of ETH FPP ENNI is autonomously sent from the Managed System. For an ETH FPP ENNI, the following information may be provided by the Carrier Ethernet Manager as part of the creation request: – FPP Type: Indicates that the ETH FPP is an ENNI. – FPP SubType (Optional): A string that indicates the detailed FPP sub-type. – User Label. – IEEE 802.3Address (Optional): The [IEEE 802.3] address which is placed in the source-address field of any non-FDFr specific Ethernet frames that originate at this interface. – Max Number of Virtual Connections (Optional). – MTU Size.
Description (cont.) | – ENNI Label: Describes the ENNI within the scope of the Ethernet provider domain. The ENNI Label attribute is a value that is assigned to the ENNI by the Ethernet Provider. – Protection Mechanism: The method for protection, if any, against a failure. – SVLAN-ID Mapping: The map that associates each S-Tagged ENNI Frame with an End Point. The End Point Type within an End Point Map for ENNI frames mapped to an OVC MUST take the value of “OVC”. The End Point Type within an End Point Map for ENNI frames mapped to a VUNI MUST take the value of “VUNI”. – Maximum Number of OVC End Points per OVC: The Maximum Number of OVC End Points per OVC provides an upper bound on the number of OVC End Points that are associated by an OVC that the Operator can support at the ENNI. Note that if the Maximum Number of OVC End Points per OVC is one, then hairpin switching cannot be supported at the ENNI. – Supported By (GET, SET BY CREATE): Relationship with supporting objects. – Client/Server (GET, SET BY CREATE): Relationship with TRANS layer TTP (Encapsulation Port). – Flow Domain Interfaces (GET, SET BY CREATE): Relationship with ETH Flow Domain that contains the FPP in a given layer. – Ingress Bandwidth Profile (Optional): This attribute indicates the ingress bandwidth profile for all ETH services at the ETH FPP ENNI in the ingress direction. – Egress Bandwidth Profile (Optional): This attribute indicates the egress bandwidth profile for all ETH services at the ETH FPP ENNI in the egress direction
Ends When | 1) Managed System returns the creation response to Carrier Ethernet Manager 2) Exception happens
Exceptions | 1) Unknown Managed Entity 2) Managed System Processing Error 3) Invalid Parameter
Post-Conditions | A new instance of ETH Flow Point Pool ENNI is created.

## Slide 20: Performance Management
Functions to control SOAM PM (MEF 35)
Loss, Delay, and Availability are covered

## Slide 21: Fault Management
Fault Management functions as defined by MEF 30
Loopback, Link Trace, Lock
Alarm and Notifications

## Slide 22: Information Model
MEF 7.2 provides MEF specific extensions to the ITU-T Q.827.1 information model

## Slide 23: MEF Specific Information Model
MEF 7.2 provides the class object diagrams for the MEF specific Carrier Ethernet Services
For example, below is the diagram for the ENNI related bandwidth profile attributes:

## Slide 24: Summary

## Slide 25: Summary MEF 7.2
MEF 7.2 provides the EMS-NMS Management Information Model
Provides the Use Cases needed for the EMS-NMS Management Interface
Provides detailed functional decomposition
Shows the linkage between the MEF specific objects and the common models from the ITU-T and TMF

## Slide 26: For Full Details …
Please visit www.metroethernetforum.org Select Information Center on Left Navigation to access the full specification and extracted MIB files
Carrier Ethernet Network
UNI
UNI
CE
CE
CE
Carrier Ethernet 2.0
EVPL Services
UNI
Carrier Ethernet 2.0
EVP-LAN Service
ISP POP
Internet
UNI
UNI
CE
CE
CE
UNI
Carrier Ethernet Network
EVC: Ethernet Virtual Connection
UNI: User Network Interface. the physical demarcation point between the responsibility of the Service Provider and the responsibility of the End-User/Subscriber
CE Customer Equipment
E-LAN Service type
E-Line Service type

## Slide 27: Accelerating Worldwide Adoption of Carrier-class Ethernet Networks and Services
www.MetroEthernetForum.org