## Slide 1: Introducing the Specifications of the MEF
MEF 40: UNI and EVC Definition of Managed Objects
April 2013

## Slide 2: MEF Reference Presentations
Intention
  These MEF reference presentations are intended to give general overviews of the MEF work and have been approved by the MEF Marketing Committee
  Further details on the topic are to be found in related specifications, technical overviews, white papers in the MEF public site Information Center: http://metroethernetforum.org/InformationCenter
  Notice
  © The Metro Ethernet Forum 2013. Any reproduction of this document, or any portion thereof, shall contain the following statement: "Reproduced with permission of the Metro Ethernet Forum." No user of this document is authorized to modify any of the information contained herein.

## Slide 3: Outline
Approved MEF Specifications
About this Specification
In Scope / Out of Scope
Terminology, Concepts & Relationship to other standards
MEF Service Lifecycle & Management Framework
UNI-EVC MIB Review
  Section Descriptions
Summary
Related Specifications

## Slide 4: Approved MEF Specifications*
Specification | Description
MEF 2 | Requirements and Framework for Ethernet Service Protection
MEF 3 | Circuit Emulation Service Definitions, Framework and Requirements in Metro Ethernet Networks
MEF 4 | Metro Ethernet Network Architecture Framework Part 1: Generic Framework
MEF 6.1 | Metro Ethernet Services Definitions Phase 2
MEF 7.2 | Carrier Ethernet Management Information Model
MEF 8 | Implementation Agreement for the Emulation of PDH Circuits over Metro Ethernet Networks
MEF 9 | Abstract Test Suite for Ethernet Services at the UNI
MEF 10.2 | Ethernet Services Attributes Phase 2
MEF 11 | User Network Interface (UNI) Requirements and Framework
MEF 12.1 | Metro Ethernet Network Architecture Framework Part 2: Ethernet Services Layer
MEF 13 | User Network Interface (UNI) Type 1 Implementation Agreement
MEF 14 | Abstract Test Suite for Traffic Management Phase 1
MEF 15 | Requirements for Management of Metro Ethernet Phase 1 Network Elements
MEF 16 | Ethernet Local Management Interface
*Current at time of publication. See MEF web site for official current list, minor updates and superseded work (such as MEF 1 and MEF 5)

## Slide 5: Approved MEF Specifications
Specification | Description
MEF 17 | Service OAM Framework and Requirements
MEF 18 | Abstract Test Suite for Circuit Emulation Services
MEF 19 | Abstract Test Suite for UNI Type 1
MEF 20 | User Network Interface (UNI) Type 2 Implementation Agreement
MEF 21 | Abstract Test Suite for UNI Type 2 Part 1: Link OAM
MEF 22.1 | Mobile Backhaul Implementation Agreement Phase 2
MEF 23.1 | Class of Service Implementation Agreement Phase 2
MEF 24 | Abstract Test Suite for UNI Type 2 Part 2: E-LMI
MEF 25 | Abstract Test Suite for UNI Type 2 Part 3: Service OAM
MEF 26.1 | External Network Network Interface (ENNI) – Phase 2
MEF 27 | Abstract Test Suite For UNI Type 2 Part 5: Enhanced UNI Attributes & Part 6: L2CP Handling
MEF 28 | External Network Network Interface (ENNI) Support for UNI Tunnel Access and Virtual UNI
MEF 29 | Ethernet Services Constructs

## Slide 6: Approved MEF Specifications
Specification | Description
MEF 30.1 | Service OAM Fault Management Implementation Agreement: Phase 2
MEF 31 | Service OAM Fault Management Definition of Managed Objects
MEF 32 | Requirements for Service Protection Across External Interfaces
MEF 33 | Ethernet Access Services Definition
MEF 34 | Abstract Test Suite for Ethernet Access Services
MEF 35 | Service OAM Performance Monitoring Implementation Agreement
MEF 36 | Service OAM SNMP MIB for Performance Monitoring
MEF 37 | Abstract Test Suite for ENNI
MEF 38 | Service OAM Fault Management YANG Modules Technical Specification
MEF 39 | Service OAM Performance Monitoring YANG Modules Technical Specifications
MEF 40 | UNI and EVC Definition of Managed Objects
*Current at time of publication. See MEF web site for official current list, minor updates (such as MEF 31.0.1 amendment to this document) and superseded work (such as MEF 1 and MEF 5)

## Slide 7: MEF Specification Overview
Standardized Services
Purpose
Specifies the SNMP UNI and EVC Management Information Base (MIB) that supports the MEF UNI and EVC defined in MEF 4, MEF 6.1, MEF 6.1.1, MEF 10.2, the management requirements in MEF 15, and the managed objects specified in MEF 7.2 and ITU-T Q.840.1. The MIB includes objects necessary to configure and monitor UNIs and EVCs via SNMP.
Audience
Applicable to entire Metro Ethernet Market including Service Providers, Access Providers, equipment vendors, and EMS/NMS/OSS vendors to provision and monitor equipment that is MEF compatible.
MEF 40 – UNI and EVC Definition of Managed Objects

## Slide 8: Overview of MEF 40

## Slide 9: About MEF 40
Purpose:
  This presentation is an introduction to MEF 40 – UNI and EVC Definition of Managed Objects
Audience
  Equipment Manufacturers building devices that will carry Carrier Ethernet Services
  Service Providers delivering Carrier Ethernet Services
  EMS/NMS/OSS tool vendors developing back office applications for managing, provisioning and monitoring Carrier Ethernet Services
Other Documents
  Presentations of other MEF specifications and an overview of all specifications is available on the MEF web site
  Other materials such as white papers and case studies are also available

## Slide 10: MEF 40 - In Scope/Out of Scope
MEF 40 requirements are primarily driven by
  Network Management requirements for ME NEs (MEF 15)
  Carrier Ethernet Common Information Model (MEF 7.2 and ITU-T Q.840.1)
MEF 40 defines functionality for managing UNI and EVC
MEF 40 does not define functionality for managing ENNI or OVC

## Slide 11: Terminology and Concepts
MEF 40 adheres to these MEF Specifications for terminology:
  Refer to MEF 6.1 for Ethernet service definitions
  Refer to MEF 6.1.1 for L2CP definition
  Refer to MEF 10.2 for EVC & UNI Service Attribute and Parameter definitions
MEF 40 relies on MEF 31 for protocol specific terminology
  Simple Network Management Protocol (SNMP)
  SNMP Manager
  Management Information Model (MIB)
  Element Management System (EMS)
  Network Management System (NMS)
  Operations Support System (OSS)

## Slide 12: Relationship with other Specifications
MEF 40

## Slide 13: MEF Service Lifecycle and SOAM
Network Management
Provisioning and Turn-up is used to bring the service “in-service”

## Slide 14: MEF Specification Section Review

## Slide 15: Introducing MEF 40
The presentation is broken into sections:
  Overview
  Network Management Concepts/Framework
  Interfaces MIB Indexing
  UNI-EVC MIB Structure
    Descriptions
  Summary
  Where to find additional information

## Slide 16: What is a MIB?
A Management Information Base (MIB), or data model, is a collection of managed objects that can be used to provision or query a network device from a management system, such as a centrally located NMS (Network Management System).
A MIB along with the management protocol, such as SNMPv2c, defines a standard network management interface for administration and maintenance of network elements.
MIB
Network Management System
Network Element
Configuration and Monitoring Data

## Slide 17: Management Framework
MIB
MIB
UNI
UNI
ENNI
CPE
CPE
Operator 1 Network
Operator 2 Network
NID
NID
Ethernet Virtual Connection
O
Network Management System
SP Network Ops
Notify
Trouble Ticket System
SNMP
SNMP
MIB
MIB
MIB
MIB

## Slide 18: Interfaces MIB Indexing
MEF 40 uses RFC 2863 ifIndex with several tables
MEF 40 supports several objects from the ifTable.
The ifType used is ethernetCsmacd(6)

## Slide 19: UNI-EVC MIB Structure
MEF-UNI-EVC-MIB defines the following groups of managed objects necessary to support configuration, status and statistics

## Slide 20: Service Interface Attributes
This group of managed objects consists of
  mefServiceInterfaceCfgTable
    Contains basic objects (type, identifier, frame format, etc.) to provision the MEF interface on the Metro Ethernet-Network Element (ME-NE)
  mefServiceInterfaceStatusTable
    Contains basic status reporting objects (type, maximum number of virtual channels, maximum number of end points per virtual channel) for the MEF interface of the ME-NE
  mefServiceInterfaceStatisticTable
    Contains various egress/ingress frame and octet counter statistics for the MEF interface of the ME-NE

## Slide 21: Service UNI Attributes
This group of managed objects consists of
  mefServiceUniCfgTable
    Contains objects (identifier, bundling, all-to-one bundling, multiplexing, CE VLAN ID, CE VLAN Priority) to provision the UNI attributes on the Metro Ethernet-Network Element (ME-NE)
  mefServiceEvcPerUniCfgTable
    Contains objects (identifier, service type, CE VLAN Map, Egress/Ingress BWP Indexes) to provision the EVC per UNI attributes on the Metro Ethernet-Network Element (ME-NE)

## Slide 22: Service EVC Attributes
This group of managed objects consists of
  mefServiceEvcCfgTable
    Contains objects (identifier, MTU size, service type, CE VLAN id preservation, CE VLAN CoS preservation, etc.) to provision the EVC attributes on the Metro Ethernet-Network Element (ME-NE)
  mefServiceEvcUniCfgTable
    Contains an object to allow configuring the UNI type (root, leaf) on an EVC
  mefServiceEvcStatusTable
    Contains basic status reporting objects (maximum MTU size, maximum number of UNIs, operational state) for the EVC of the ME-NE

## Slide 23: Service Bandwidth Profile Attributes
This group of managed objects consists of
  mefServiceBwpCfgTable
    Contains objects (CIR, EIR, CBS, EBS, CF, CM, etc.) to provision a Bandwidth Profile (BWP) as well as associate the BWP with a CoS ID.
  mefServiceBwpGrpCfgTable
    Contains objects to support BWP group settings

## Slide 24: Class of Service Attributes
This group of managed objects consists of
  mefServiceCosCfgTable
    Contains objects (identifier, type, identifier list, L2CP destination MAC Address, L2CP Ethernet Protocol, L2CP Subtype) to provision a Class of Service Identifier profile

## Slide 25: Service L2CP Attributes
This group of managed objects consists of
  mefServiceL2cpCfgTable
    Contains objects (type, matching scope, destination MAC address, L2CP Ethernet Protocol, L2CP Subtype) to provision an L2CP profile
  mefServiceL2cpGrpCfgTable
    Contains objects to support L2CP group settings

## Slide 26: Service Performance Attributes
This group of managed objects consists of
  mefServicePerformanceTable
    Contains basic objects to support Traffic Performance Data Set profile settings on a Bandwidth Profile (e.g., green, yellow, red frame/octet counters)

## Slide 27: Service Notification Attributes
This group of managed objects consists of
  Contains an object to enable/disable SNMP notifications
  Contains objects carried within the payload of SNMP notifications (date, time, configuration change type)
  Contains the SNMP Notification which can be triggered when the configuration of an object is added, deleted or modified

## Slide 28: Summary

## Slide 29: Summary MEF 40
MEF 40 defines the managed objects for using an SNMP management interface for configuring the UNI and EVC reference points of a CEN
  In addition, managed objects are defined for retrieving configuration status and statistics for the UNI and EVC reference points
MEF 40 enables MEF equipment providers to provide a standardized management interface for the UNI and EVC for
  Configuration Management
  Interface Network Monitoring

## Slide 30: Related Specifications
MEF 6.1 – Ethernet Services Definitions (Phase 2)
MEF 6.1.1 – Layer 2 Control Protocol Handling Amendment
MEF 7.2 – Carrier Ethernet Management Information Model
MEF 10.2 – Ethernet Services Attributes (Phase 2)
MEF 15 – Requirements for Management of Metro Ethernet Phase 1 Network Elements
IETF RFC 2863 – The Interfaces Group MIB (IF-MIB)

## Slide 31: Final Word
Configuration Management
  In the context of MEF 40, data models (MIBs) are defined that support UNI and EVC configuration management in CENs
Next Actions (For Further Information)
  Read the full MEF 40 technical specification and familiarize yourself with the set of defined managed objects
  Read the full MEF 6.1 and MEF 10.2 specifications (note, review of MEF 7.2 and MEF 15 may also be helpful)
  Understand the principal Interfaces Group (IF-MIB) managed objects, indexing and capabilities
Notes: This section goes into further detail in detailing the defined Service Attributes and parameters requirement and recommendations as specified for each of the defined services: EPL, EVPL and E-LAN.
(Refer to the Specs and the accompanying Ethernet Service Description document for more details)

## Slide 32: For Full Details …
Please visit www.metroethernetforum.org Select Information Center on Left Navigation to access the full specification and extracted MIB files
Carrier Ethernet Network
UNI
UNI
CE
CE
CE
Carrier Ethernet 2.0
EVPL Services
UNI
Carrier Ethernet 2.0
EVP-LAN Service
ISP POP
Internet
UNI
UNI
CE
CE
CE
UNI
Carrier Ethernet Network
EVC: Ethernet Virtual Connection
UNI: User Network Interface. the physical demarcation point between the responsibility of the Service Provider and the responsibility of the End-User/Subscriber
CE Customer Equipment
E-LAN Service type
E-Line Service type

## Slide 33: Accelerating Worldwide Adoption of Carrier-class Ethernet Networks and Services
www.MetroEthernetForum.org